## Slide 1: Advanced Computer Architecture Fall 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 2

## Slide 2: Copyright Notice
Lectures adopted from
Computer Architecture: A Quantitative Approach, 5th edition, John L. Hennessy,‎ David A. Patterson, MK pub., 2019
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran

## Slide 3
Chapter 1
Fundamentals of Quantitative Design and Analysis
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 4: Computer Technology
Performance improvements:
  Improvements in semiconductor technology
    Feature size, clock speed
  Improvements in computer architectures
    Enabled by HLL compilers, UNIX
    Lead to RISC architectures
  Together have enabled:
    Lightweight computers
    Productivity-based managed/interpreted programming languages
Introduction

## Slide 5: Current Trends in Architecture
Cannot continue to leverage Instruction-Level parallelism (ILP)
  Single processor performance improvement ended in 2003
New models for performance:
  Data-level parallelism (DLP)
  Thread-level parallelism (TLP)
  Request-level parallelism (RLP)
These require explicit restructuring of the application
Introduction

## Slide 6: Parallelism
Classes of parallelism in applications:
  Data-Level Parallelism (DLP)
  Task-Level Parallelism (TLP)
Classes of architectural parallelism:
  Instruction-Level Parallelism (ILP)
  Vector architectures/Graphic Processor Units (GPUs)
  Thread-Level Parallelism
  Request-Level Parallelism
Classes of Computers

## Slide 7: Flynn’s Taxonomy
Single instruction stream, single data stream (SISD)
Single instruction stream, multiple data streams (SIMD)
  Vector architectures
  Multimedia extensions
  Graphics processor units
Multiple instruction streams, single data stream (MISD)
  No commercial implementation
Multiple instruction streams, multiple data streams (MIMD)
  Tightly-coupled MIMD
  Loosely-coupled MIMD
Classes of Computers

## Slide 8: Computer Architecture Topics
Instruction Set Architecture
Pipelining, Hazard Resolution,
Superscalar, Reordering,
Prediction, Speculation,
Vector, DSP
Addressing,
Protection,
Exception Handling
L1 Cache
L2 Cache
DRAM
Disks, WORM, Tape
Coherence,
Bandwidth,
Latency
Emerging Technologies
Interleaving
Bus protocols
RAID
VLSI
Input/Output and Storage
Memory
Hierarchy
Pipelining and Instruction
Level Parallelism

## Slide 9: Defining Computer Architecture
“Old” view of computer architecture:
  Instruction Set Architecture (ISA) design
  i.e. decisions regarding:
    registers, memory addressing, addressing modes, instruction operands, available operations, control flow instructions, instruction encoding
“Real” computer architecture:
  Specific requirements of the target machine
  Design to maximize performance within constraints: cost, power, and availability
  Includes ISA, microarchitecture, hardware
Defining Computer Architecture

## Slide 10: Trends in Technology
Integrated circuit technology (Moore’s Law)
  Transistor density: 35%/year
  Die size: 10-20%/year
  Integration overall: 40-55%/year
DRAM capacity: 25-40%/year (slowing)
  8 Gb (2014), 16 Gb (2019), possibly no 32 Gb
Flash capacity: 50-60%/year
  8-10X cheaper/bit than DRAM
Magnetic disk capacity: recently slowed to 5%/year
  Density increases may no longer be possible, maybe increase from 7 to 9 platters
  8-10X cheaper/bit then Flash
  200-300X cheaper/bit than DRAM
Trends in Technology

## Slide 11: Bandwidth and Latency
Bandwidth or throughput
  Total work done in a given time
  32,000-40,000X improvement for processors
  300-1200X improvement for memory and disks
Latency or response time
  Time between start and completion of an event
  50-90X improvement for processors
  6-8X improvement for memory and disks
Trends in Technology

## Slide 12: Bandwidth and Latency
Log-log plot of bandwidth and latency milestones
Trends in Technology

## Slide 13: Transistors and Wires
Feature size
  Minimum size of transistor or wire in x or y dimension
  10 microns in 1971 to .011 microns in 2017
  Transistor performance scales linearly
    Wire delay does not improve with feature size!
  Integration density scales quadratically
Trends in Technology

## Slide 14: Power and Energy
Thermal Design Power (TDP)
  Maximum amount of heat generated by a chip
  Characterizes sustained power consumption
  Used as target for power supply and cooling system
  Lower than peak power (1.5X higher), higher than average power consumption
Clock rate can be reduced dynamically to limit power consumption
Energy per task is often a better measurement
Trends in Power and Energy

## Slide 15: Dynamic Energy and Power
Dynamic energy
  Transistor switch from 0 → 1 or 1 → 0
  ½ x Capacitive load x Voltage2
Dynamic power
  ½ x Capacitive load x Voltage2 x Frequency switched
Reducing clock rate reduces power, not energy
Trends in Power and Energy

## Slide 16: Power
Intel 80386 consumed ~ 2 W
3.3 GHz Intel Core i7 consumes 130 W
Heat must be dissipated from 1.5 x 1.5 cm chip
This is the limit of what can be cooled by air
Trends in Power and Energy

## Slide 17: Reducing Power
Techniques for reducing power:
  Do nothing well
  Dynamic Voltage-Frequency Scaling
  Low power state for DRAM, disks
  Overclocking, turning off cores
Trends in Power and Energy

## Slide 18: Static Power
Static power consumption
  25-50% of total power
  Currentstatic x Voltage
  Scales with number of transistors
  To reduce: power gating
Trends in Power and Energy

## Slide 19: Measuring Performance
Typical performance metrics:
  Response time
  Throughput
Speedup of X relative to Y
  Execution timeY / Execution timeX
Execution time
  Wall clock time: includes all system overheads
  CPU time: only computation time
Benchmarks
  Kernels (e.g. matrix multiply)
  Toy programs (e.g. sorting)
  Synthetic benchmarks (e.g. Dhrystone)
  Benchmark suites (e.g. SPEC06fp, TPC-C)
Measuring Performance