## Slide 1: Advanced Computer Architecture Fall 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 4

## Slide 2: Copyright Notice
Lectures adopted from
Graduate Computer Architecture, handouts, by Prof. Samira Khan, University of Virginia, Fall 2017.
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran

## Slide 3: Prefetching: Outline
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Why prefetch? Why could/does it work?
The four questions
  What (to prefetch), when, where, how
Software prefetching algorithms
Hardware prefetching algorithms
Prefetching performance
  Coverage, accuracy, timeliness
  Bandwidth consumption, cache pollution

## Slide 4: Prefetching
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Idea: Fetch the data before it is needed (i.e. pre-fetch) by the program
Why?
  Memory latency is high. If we can prefetch accurately and early enough we can reduce/eliminate that latency.
  Can eliminate compulsory cache misses
  Can it eliminate all cache misses? Capacity, conflict?
Involves predicting which address will be needed in the future
  Works if programs have predictable miss address patterns

## Slide 5: Prefetching and Correctness
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Does a misprediction in prefetching affect correctness?
No, prefetched data at a “mispredicted” address is simply not used
There is no need for state recovery
  In contrast to branch misprediction or value misprediction

## Slide 6: Basics
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
In modern systems, prefetching is usually done in cache block granularity
Prefetching is a technique that can reduce both
  Miss rate
  Miss latency
Prefetching can be done by
  hardware
  compiler
  programmer

## Slide 7: Prefetching: The Four Questions
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
What
  What addresses to prefetch
When
  When to initiate a prefetch request
Where
  Where to place the prefetched data
How
  Software, hardware, execution-based, cooperative

## Slide 8: Challenges in Prefetching: What
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
What addresses to prefetch
  Prefetching useless data wastes resources
    Memory bandwidth
    Cache or prefetch buffer space
    Energy consumption
    These could all be utilized by demand requests or more accurate prefetch requests
  Accurate prediction of addresses to prefetch is important
    Prefetch accuracy = used prefetches / sent prefetches
How do we know what to prefetch
  Predict based on past access patterns
  Use the compiler’s knowledge of data structures
Prefetching algorithm determines what to prefetch

## Slide 9: Challenges in Prefetching: When
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
When to initiate a prefetch request
  Prefetching too early
    Prefetched data might not be used before it is evicted from storage
  Prefetching too late
    Might not hide the whole memory latency
When a data item is prefetched affects the timeliness of the prefetcher

## Slide 10: Challenges in Prefetching: Where
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Where to place the prefetched data
  In cache
    + Simple design, no need for separate buffers
    -- Can evict useful demand data  cache pollution
  In a separate prefetch buffer
    + Demand data protected from prefetches  no cache pollution
    -- More complex memory system design
    - Where to place the prefetch buffer
    - When to access the prefetch buffer (parallel vs. serial with cache)
    - When to move the data from the prefetch buffer to cache
    - How to size the prefetch buffer
    - Keeping the prefetch buffer coherent
Many modern systems place prefetched data into the cache
  Intel Pentium 4, Core2’s, AMD systems, IBM POWER4,5,6, …

## Slide 11: Challenges in Prefetching: Where
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Which level of cache to prefetch into?
  Memory to L2, memory to L1. Advantages/disadvantages?
  L2 to L1? (a separate prefetcher between levels)
Where to place the prefetched data in the cache?
  Do we treat prefetched blocks the same as demand-fetched blocks?
  Prefetched blocks are not known to be needed
    With LRU, a demand block is placed into the MRU position
Do we skew the replacement policy such that it favors the demand-fetched blocks?
  E.g., place all prefetches into the LRU position in a way?

## Slide 12: Challenges in Prefetching: Where
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Where to place the hardware prefetcher in the memory hierarchy?
  In other words, what access patterns does the prefetcher see?
  L1 hits and misses
  L1 misses only
  L2 misses only
Seeing a more complete access pattern:
  + Potentially better accuracy and coverage in prefetching
  -- Prefetcher needs to examine more requests (bandwidth intensive, more ports into the prefetcher?)

## Slide 13: Challenges in Prefetching: How
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Software prefetching
  ISA provides prefetch instructions
  Programmer or compiler inserts prefetch instructions (effort)
  Usually works well only for “regular access patterns”
Hardware prefetching
  Hardware monitors processor accesses
  Memorizes or finds patterns/strides
  Generates prefetch addresses automatically
Execution-based prefetchers
  A “thread” is executed to prefetch data for the main program
  Can be generated by either software/programmer or hardware

## Slide 14: Hardware Prefetching
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Idea: Specialized hardware observes load/store access patterns and prefetches data based on past access behavior
Tradeoffs:
  + Can be tuned to system implementation
  + Does not waste instruction execution bandwidth
  -- More hardware complexity to detect patterns
  - Software can be more efficient in some cases

## Slide 15: Next-Line Prefetchers
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Simplest form of hardware prefetching: always prefetch next N cache lines after a demand access (or a demand miss)
  Next-line prefetcher (or next sequential prefetcher)
  Tradeoffs:
    + Simple to implement. No need for sophisticated pattern detection
    + Works well for sequential/streaming access patterns (instructions?)
    -- Can waste bandwidth with irregular patterns
    -- And, even regular patterns:
    - What is the prefetch accuracy if access stride = 2 and N = 1?
    - What if the program is traversing memory from higher to lower addresses?
    - Also prefetch “previous” N cache lines?

## Slide 16: Stride Prefetchers
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
Two kinds
  Instruction program counter (PC) based
  Cache block address based
Instruction based:
  Baer and Chen, “An effective on-chip preloading scheme to reduce data access penalty,” SC 1991.
  Idea:
    Record the distance between the memory addresses referenced by a load instruction (i.e. stride of the load) as well as the last address referenced by the load
    Next time the same load instruction is fetched, prefetch last address + stride