## Slide 1: Advanced Computer Architecture Fall 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 5

## Slide 2: Copyright Notice
Lectures adopted from
Computer Architecture: A Quantitative Approach, 5th edition, John L. Hennessy,‎ David A. Patterson, MK pub., 2019
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran

## Slide 3
Chapter 3
Instruction-Level Parallelism and Its Exploitation
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 4: Introduction
Pipelining become universal technique in 1985
  Overlaps execution of instructions
  Exploits “Instruction Level Parallelism”
Beyond this, there are two main approaches:
  Hardware-based dynamic approaches
    Used in server and desktop processors
    Not used as extensively in PMD processors
  Compiler-based static approaches
    Not as successful outside of scientific applications
Introduction

## Slide 5: Instruction-Level Parallelism
When exploiting instruction-level parallelism, goal is to minimize CPI
  Pipeline CPI =
    Ideal pipeline CPI +
    Structural stalls +
    Data hazard stalls +
    Control stalls
Parallelism with basic block is limited
  Typical size of basic block = 3-6 instructions
  Must optimize across branches
Introduction

## Slide 6: Data Dependence
Loop-Level Parallelism
  Unroll loop statically or dynamically
  Use SIMD (vector processors and GPUs)
Challenges
  Data dependency
    Instruction j is data dependent on instruction i if
      Instruction i produces a result that may be used by instruction j
      Instruction j is data dependent on instruction k and instruction k is data dependent on instruction i
Dependent instructions cannot be executed simultaneously
Introduction

## Slide 7: Data Dependence
Dependencies are a property of programs
Pipeline organization determines if dependence is detected and if it causes a stall
Data dependence conveys:
  Possibility of a hazard
  Order in which results must be calculated
  Upper bound on exploitable instruction level parallelism
Dependencies that flow through memory locations are difficult to detect
Introduction

## Slide 8: Name Dependence
Two instructions use the same name but no flow of information
  Not a true data dependence, but is a problem when reordering instructions
  Antidependence: instruction j writes a register or memory location that instruction i reads
    Initial ordering (i before j) must be preserved
  Output dependence: instruction i and instruction j write the same register or memory location
    Ordering must be preserved
To resolve, use register renaming techniques
Introduction

## Slide 9: Other Factors
Data Hazards
  Read after write (RAW)
  Write after write (WAW)
  Write after read (WAR)
Control Dependence
  Ordering of instruction i with respect to a branch instruction
    Instruction control dependent on a branch cannot be moved before the branch so that its execution is no longer controlled by the branch
    An instruction not control dependent on a branch cannot be moved after the branch so that its execution is controlled by the branch
Introduction

## Slide 10: Examples
or instruction dependent on add and sub
Assume x4 isn’t used after skip
  Possible to move sub before the branch
Introduction
Example 1:
add x1,x2,x3
beq x4,x0,L
sub x1,x1,x6
L: …
or x7,x1,x8
Example 2:
add x1,x2,x3
beq x12,x0,skip
sub x4,x5,x6
add x5,x4,x9
skip:
or x7,x8,x9