## Slide 1: Advanced Computer Architecture Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 5

## Slide 2: Copyright Notice
Lectures adopted from
Computer Architecture: A Quantitative Approach, 5th edition, John L. Hennessy,‎ David A. Patterson, MK pub., 2019
Advanced Computer Architecture-Spring 2018, AUT, Tehran, Iran

## Slide 3
Chapter 3
Instruction-Level Parallelism and Its Exploitation
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 4: Dynamic Scheduling
Rearrange order of instructions to reduce stalls while maintaining data flow
Advantages:
  Compiler doesn’t need to have knowledge of microarchitecture
  Handles cases where dependencies are unknown at compile time
Disadvantage:
  Substantial increase in hardware complexity
  Complicates exceptions
Dynamic Scheduling

## Slide 5: Dynamic Scheduling
Dynamic scheduling implies:
  Out-of-order execution
  Out-of-order completion
Example 1:
  fdiv.d f0,f2,f4
  fadd.d f10,f0,f8
  fsub.d f12,f8,f14
  fsub.d is not dependent, issue before fadd.d
Dynamic Scheduling

## Slide 6: Dynamic Scheduling
Example 2:
  fdiv.d f0,f2,f4
  fmul.d f6,f0,f8
  fadd.d f0,f10,f14
  fadd.d is not dependent, but the antidependence makes it impossible to issue earlier without register renaming
Dynamic Scheduling

## Slide 7: Register Renaming
Example 3:
fdiv.d f0,f2,f4
fadd.d f6,f0,f8
fsd f6,0(x1)
fsub.d f8,f10,f14
fmul.d f6,f10,f8
  name dependence with f6
antidependence
antidependence
Dynamic Scheduling

## Slide 8: Register Renaming
Example 3:
fdiv.d f0,f2,f4
fadd.d S,f0,f8
fsd S,0(x1)
fsub.d T,f10,f14
fmul.d f6,f10,T
Now only RAW hazards remain, which can be strictly ordered
Dynamic Scheduling

## Slide 9: Out of Order with Scoreboard
All instructions pass through the issue stage in order
  Can be stalled or bypass each other in the second stage
Scoreboarding
  Allowing instructions to execute out of order when there are sufficient resources and no data dependences
  The scoreboard takes full responsibility for instruction issue and execution, including all hazard detection
  Multiple functional units
  Pipelined functional units
Dynamic Scheduling

## Slide 10: Out of Order with Scoreboard
The scoreboard determines when the instruction can read its operands and begin execution
  It monitors every change in the hardware
Scoreboard controls when an instruction can write its result into the destination register
  All hazard detection and resolution are centralized in the scoreboard
Dynamic Scheduling

## Slide 11: Out of Order with Scoreboard
Instruction steps in Scoreboard
  Issue (structural and WAW hazards)
    If a functional unit for the instruction is free and no other active instruction has the same destination register
  Read operands (RAW hazard)
    Monitors the availability of the source operands
  Execution
    Begins execution upon receiving operands and notifies the scoreboard when the result is ready
  Write result
    Checks for WAR hazards and stalls the completing instruction, if necessary
Dynamic Scheduling

## Slide 12: Out of Order with Scoreboard
Dynamic Scheduling

## Slide 13: Out of Order with Scoreboard
Dynamic Scheduling
Scoreboarding is a single-issue scheme
  A WAW or a structural hazard (an unavailable FU) prevent proceeding the instruction from the IS to the RO stage
    No other instruction can be issued (an in-order issue scheme)
  A RAW hazard prevents an instruction proceeding from the RO to the EX stage
  A WAR hazard prevents result write-back
  After the issue to the FU, the FU is blocked until the instruction is dispatched and execution starts

## Slide 14: OOO Exe with Tomasulo
Tomasulo’s Approach
  Tracks when operands are available
  Introduces register renaming in hardware
    Minimizes WAW and WAR hazards
  The technique that dynamically eliminates name dependences to avoid WAR and WAW hazards is called register renaming
  The centralized scoreboard is replaced with distributed control within the processor
Register renaming is provided by reservation stations (RS)
  Contains:
    The instruction
    Buffered operand values (when available)
    Reservation station number of instruction providing the operand values
Dynamic Scheduling

## Slide 15: Register Renaming
RS fetches and buffers an operand as soon as it becomes available (not necessarily involving register file)
Pending instructions designate the RS to which they will send their output
  Result values broadcast on a result bus, called the common data bus (CDB)
Only the last output updates the register file
As instructions are issued, the register specifiers are renamed with the reservation station
May be more reservation stations than registers
Load and store buffers
  Contain data and addresses, act like reservation stations
Dynamic Scheduling

## Slide 16: Tomasulo’s Algorithm
Dynamic Scheduling

## Slide 17: Tomasulo’s Algorithm
Three Steps:
  Issue
    Get next instruction from FIFO queue
    If available RS, issue the instruction to the RS with operand values if available
    If operand values not available, stall the instruction
  Execute
    When operand becomes available, store it in any reservation stations waiting for it
    When all operands are ready, issue the instruction
    Loads and store maintained in program order through effective address
    No instruction allowed to initiate execution until all branches that proceed it in program order have completed
  Write result
    Write result on CDB into reservation stations and store buffers
      (Stores must wait until address and value are received)
Dynamic Scheduling

## Slide 18: Example
Dynamic Scheduling

## Slide 19: Tomasulo’s Algorithm
Example loop:
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,8
bne x1,x2,Loop // branches if x16 != x2
Dynamic Scheduling

## Slide 20: Tomasulo’s Algorithm
Dynamic Scheduling

## Slide 21: Tomasulo vs. Scoreboard
Dynamic Scheduling
In-order issue
Scoreboard is stalled on WAW and WAR
Operand forwarding in Tomasulo
Hardware complexity of Tomasulo