## Slide 1: Advanced Computer Architecture Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 5

## Slide 2: Copyright Notice
Lectures adopted from
Computer Architecture: A Quantitative Approach, 5th edition, John L. Hennessy,‎ David A. Patterson, MK pub., 2019
Advanced Computer Architecture-Spring 2018, AUT, Tehran, Iran

## Slide 3
Chapter 3
Instruction-Level Parallelism and Its Exploitation
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 4: Multiple Issue and Static Scheduling
To achieve CPI < 1, need to complete multiple instructions per clock
Solutions:
  Statically scheduled superscalar processors
  VLIW (very long instruction word) processors
  Dynamically scheduled superscalar processors
Multiple Issue and Static Scheduling

## Slide 5: Multiple Issue
Multiple Issue and Static Scheduling

## Slide 6: VLIW Processors
Package multiple operations into one instruction
Example VLIW processor:
  One integer instruction (or branch)
  Two independent floating-point operations
  Two independent memory references
Must be enough parallelism in code to fill the available slots
Multiple Issue and Static Scheduling

## Slide 7: VLIW Processors
Disadvantages:
  Statically finding parallelism
  Code size
  No hazard detection hardware
  Binary code compatibility
Multiple Issue and Static Scheduling

## Slide 8: Dynamic Scheduling, Multiple Issue, and Speculation
Modern microarchitectures:
  Dynamic scheduling + multiple issue + speculation
Two approaches:
  Assign reservation stations and update pipeline control table in half clock cycles
    Only supports 2 instructions/clock
  Design logic to handle any possible dependencies between the instructions
Issue logic is the bottleneck in dynamically scheduled superscalars
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 9: Overview of Design
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 10: Multiple Issue
Examine all the dependencies among the instructions in the bundle
If dependencies exist in bundle, encode them in reservation stations
Also need multiple completion/commit
To simplify RS allocation:
  Limit the number of instructions of a given class that can be issued in a “bundle”, i.e. on FP, one integer, one load, one store
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 11: Example
Loop: ld x2,0(x1) //x2=array element
addi x2,x2,1 //increment x2
sd x2,0(x1) //store result
addi x1,x1,8 //increment pointer
bne x2,x3,Loop //branch if not last
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 12: Example (No Speculation)
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 13: Example (Mutiple Issue with Speculation)
Dynamic Scheduling, Multiple Issue, and Speculation