## Slide 1
Chapter 4
Data-Level Parallelism in Vector, SIMD, and GPU Architectures
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Introduction
SIMD architectures can exploit significant data-level parallelism for:
  Matrix-oriented scientific computing
  Media-oriented image and sound processors
SIMD is more energy efficient than MIMD
  Only needs to fetch one instruction per data operation
  Makes SIMD attractive for personal mobile devices
SIMD allows programmer to continue to think sequentially
Introduction

## Slide 3: SIMD Parallelism
Vector architectures
SIMD extensions
Graphics Processor Units (GPUs)
For x86 processors:
  Expect two additional cores per chip per year
  SIMD width to double every four years
  Potential speedup from SIMD to be twice that from MIMD!
Introduction

## Slide 4: Vector Architectures
Basic idea:
  Read sets of data elements into “vector registers”
  Operate on those registers
  Disperse the results back into memory
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth
Vector Architectures

## Slide 5: VMIPS
Example architecture: RV64V
  Loosely based on Cray-1
  32 64-bit vector registers
    Register file has 16 read ports and 8 write ports
  Vector functional units
    Fully pipelined
    Data and control hazards are detected
  Vector load-store unit
    Fully pipelined
    One word per clock cycle after initial latency
  Scalar registers
    31 general-purpose registers
    32 floating-point registers
Vector Architectures

## Slide 6: VMIPS
Vector Architectures

## Slide 7: VMIPS Instructions
.vv: two vector operands
.vs and .sv: vector and scalar operands
LV/SV: vector load and vector store from address
Example: DAXPY
8 instructions, 258 for RV64V (scalar code)
Vector Architectures

## Slide 8: Vector Execution Time
Execution time depends on three factors:
  Length of operand vectors
  Structural hazards
  Data dependencies
RV64V functional units consume one element per clock cycle
  Execution time is approximately the vector length
Convoy
  Set of vector instructions that could potentially execute together
Vector Architectures

## Slide 9: Chimes
Sequences with read-after-write dependency hazards placed in same convey via chaining
Chaining
  Allows a vector operation to start as soon as the individual elements of its vector source operand become available
Chime
  Unit of time to execute one convey
  m convoys executes in m chimes for vector length n
  For vector length of n, requires m x n clock cycles
Vector Architectures

## Slide 10: Example
vld v0,x5 # Load vector X
vmul v1,v0,f0 # Vector-scalar multiply
vld v2,x6 # Load vector Y
vadd v3,v1,v2 # Vector-vector add
vst v3,x6 # Store the sum
Convoys:
1 vld vmul
2 vld vadd
3 vst
3 chimes, 2 FP ops per result, cycles per FLOP = 1.5
For 64 element vectors, requires 32 x 3 = 96 clock cycles
Vector Architectures

## Slide 11: Multiple Lanes
Element n of vector register A is “hardwired” to element n of vector register B
  Allows for multiple hardware lanes
Vector Architectures

## Slide 12: Vector Length Register
for (i=0; i <n; i=i+1) Y[i] = a * X[i] + Y[i];
  vsetdcfg 2 DP FP # Enable 2 64b Fl.Pt. registers
  fld f0,a # Load scalar a
  loop: setvl t0,a0 # vl = t0 = min(mvl,n)
  vld v0,x5 # Load vector X
  slli t1,t0,3 # t1 = vl * 8 (in bytes)
  add x5,x5,t1 # Increment pointer to X by vl*8
  vmul v0,v0,f0 # Vector-scalar mult
  vld v1,x6 # Load vector Y
  vadd v1,v0,v1 # Vector-vector add
  sub a0,a0,t0 # n -= vl (t0)
  vst v1,x6 # Store the sum into Y
  add x6,x6,t1 # Increment pointer to Y by vl*8
  bnez a0,loop # Repeat if n != 0
  vdisable # Disable vector regs
Vector Architectures

## Slide 13: Vector Mask Registers
Consider:
for (i = 0; i < 64; i=i+1)
if (X[i] != 0)
X[i] = X[i] – Y[i];
Use predicate register to “disable” elements:
  vsetdcfg 2*FP64 # Enable 2 64b FP vector regs
  vsetpcfgi 1 # Enable 1 predicate register
  vld v0,x5 # Load vector X into v0
  vld v1,x6 # Load vector Y into v1
  fmv.d.x f0,x0 # Put (FP) zero into f0
  vpne p0,v0,f0 # Set p0(i) to 1 if v0(i)!=f0
  vsub v0,v0,v1 # Subtract under vector mask
  vst v0,x5 # Store the result in X
  vdisable # Disable vector registers
  vpdisable # Disable predicate registers
Vector Architectures

## Slide 14: SIMD Extensions
Media applications operate on data types narrower than the native word size
  Example: disconnect carry chains to “partition” adder
Limitations, compared to vector instructions:
  Number of data operands encoded into op code
  No sophisticated addressing modes (strided, scatter-gather)
  No mask registers
SIMD Instruction Set Extensions for Multimedia

## Slide 15: SIMD Implementations
Implementations:
  Intel MMX (1996)
    Eight 8-bit integer ops or four 16-bit integer ops
  Streaming SIMD Extensions (SSE) (1999)
    Eight 16-bit integer ops
    Four 32-bit integer/fp ops or two 64-bit integer/fp ops
  Advanced Vector Extensions (2010)
    Four 64-bit integer/fp ops
  AVX-512 (2017)
    Eight 64-bit integer/fp ops
  Operands must be consecutive and aligned memory locations
SIMD Instruction Set Extensions for Multimedia