## Slide 1: Advanced Computer Architecture Fall 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering and Information Technology
Amirkabir University of Technology
Lecture 7

## Slide 2: Copyright Notice
Lectures adopted from
Computer Architecture: A Quantitative Approach, 5th edition, John L. Hennessy,‎ David A. Patterson, MK pub., 2019
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran

## Slide 3
Chapter 5
Thread-Level Parallelism
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 4: Introduction
Thread-Level parallelism
  Have multiple program counters
  Uses MIMD model
  Targeted for tightly-coupled shared-memory multiprocessors
For n processors, need n threads
Amount of computation assigned to each thread = grain size
  Threads can be used for data-level parallelism, but the overheads may outweigh the benefit
Introduction

## Slide 5: Types
Symmetric multiprocessors (SMP)
  Small number of cores
  Share single memory with uniform memory latency
Distributed shared memory (DSM)
  Memory distributed among processors
  Non-uniform memory access/latency (NUMA)
  Processors connected via direct (switched) and non-direct (multi-hop) interconnection networks
Introduction

## Slide 6: Cache Coherence
Processors may see different values through their caches:
Centralized Shared-Memory Architectures

## Slide 7: Cache Coherence
Coherence
  All reads by any processor must return the most recently written value
  Writes to the same location by any two processors are seen in the same order by all processors
Consistency
  When a written value will be returned by a read
  If a processor writes location A followed by location B, any processor that sees the new value of B must also see the new value of A
Centralized Shared-Memory Architectures

## Slide 8: Enforcing Coherence
Coherent caches provide:
  Migration: movement of data
  Replication: multiple copies of data
Cache coherence protocols
  Directory based
    Sharing status of each block kept in one location
  Snooping
    Each core tracks sharing status of each block
Centralized Shared-Memory Architectures

## Slide 9: Snoopy Coherence Protocols
Write invalidate
  On write, invalidate all other copies
  Use bus itself to serialize
    Write cannot complete until bus access is obtained
Write update
  On write, update all copies
Centralized Shared-Memory Architectures

## Slide 10: Snoopy Coherence Protocols
Locating an item when a read miss occurs
  In write-back cache, the updated value must be sent to the requesting processor
Cache lines marked as shared or exclusive/modified
  Only writes to shared lines need an invalidate broadcast
    After this, the line is marked as exclusive
Centralized Shared-Memory Architectures

## Slide 11: Snoopy Coherence Protocols
Centralized Shared-Memory Architectures

## Slide 12: Snoopy Coherence Protocols
Centralized Shared-Memory Architectures

## Slide 13: MESI Protocol
Centralized Shared-Memory Architectures
write

## Slide 14: MOESI Protocol
Centralized Shared-Memory Architectures
write