## Slide 1: Advanced Computer Architecture Fall 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering and Information Technology
Amirkabir University of Technology
Lecture 7

## Slide 2: Copyright Notice
Lectures adopted from
Computer Architecture: A Quantitative Approach, 5th edition, John L. Hennessy,‎ David A. Patterson, MK pub., 2019
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran

## Slide 3
Chapter 5
Thread-Level Parallelism
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 4: Cache inclusion policy
Inclusive Policy
Exclusive Policy
Non-inclusive non-exclusive (NINE)
Centralized Shared-Memory Architectures

## Slide 5: Directory Protocols
Snooping schemes require communication among all caches on every cache miss
  Limits scalability
  Another approach: Use centralized directory to keep track of every block
    Which caches have each block
    Dirty status of each block
Implement in shared L3 cache
  Keep bit vector of size = # cores for each block in L3
Distributed Shared Memory and Directory-Based Coherence

## Slide 6: Directory Protocols
Alternative approach:
  Distribute memory
Distributed Shared Memory and Directory-Based Coherence

## Slide 7: Directory Protocols
For each block, maintain state:
  Shared
    One or more nodes have the block cached, value in memory is up-to-date
    Set of node IDs
  Uncached
  Modified
    Exactly one node has a copy of the cache block, value in memory is out-of-date
    Owner node ID
Directory maintains block states and sends invalidation messages
Distributed Shared Memory and Directory-Based Coherence

## Slide 8: Messages
Distributed Shared Memory and Directory-Based Coherence

## Slide 9: Directory Protocols
Distributed Shared Memory and Directory-Based Coherence

## Slide 10: Directory Protocols
For uncached block:
  Read miss
    Requesting node is sent the requested data and is made the only sharing node, block is now shared
  Write miss
    The requesting node is sent the requested data and becomes the sharing node, block is now exclusive
For shared block:
  Read miss
    The requesting node is sent the requested data from memory, node is added to sharing set
  Write miss
    The requesting node is sent the value, all nodes in the sharing set are sent invalidate messages, sharing set only contains requesting node, block is now exclusive
Distributed Shared Memory and Directory-Based Coherence

## Slide 11: Directory Protocols
For exclusive block:
  Read miss
    The owner is sent a data fetch message, block becomes shared, owner sends data to the directory, data written back to memory, sharers set contains old owner and requestor
  Data write back
    Block becomes uncached, sharer set is empty
  Write miss
    Message is sent to old owner to invalidate and send the value to the directory, requestor becomes new owner, block remains exclusive
Distributed Shared Memory and Directory-Based Coherence